# eDIN #1003 Contact Closure Module  Specifications

# Version 2.0

July 2013

# SUBJECT TO CHANGE WITHOUT NOTICE

1.0	General

1.1	The eDIN Contact Closure Module shall be a DMX512-controllable, contact closure output interface.

1.2	Each module shall provide twelve (12) individual Form-C relay contact closures, each controlled by a discrete DMX channel.

1.3	The relay contacts shall be capable of switching signal level voltages and currents only.

1.4	The Module shall be designed to mount on 35mm DIN rail.

2.0	Features

2.1	The module shall have several user-selectable operating modes, including but not limited to:

2.1.1 	Maintained 12 channel mode.  Each relay shall be maintained “on” while its associated DMX channel is above 50%.

2.1.2	Momentary 12 channel mode.  Each relay shall close for 100mSec when its associated DMX channel level passes through 50%, increasing or decreasing.

2.1.3 	Momentary ‘ON’ 12 channel mode.  Each relay shall close for 100mSec when its associated DMX channel passes through 50%, increasing only.

2.1.4	Momentary Split, 6 channel mode.  Each adjacent pair of relays shall be associated with a single DMX control channel.  The lower (odd-numbered) relay shall close for 100mSec when the associated DMX channel passes through 50%, increasing.  The higher (even-numbered) relay shall close for 100mSec when the associated DMX channel passes through 50%, decreasing.

2.1.5	Maintained Split, 6 channel mode.  Each adjacent pair of relays shall be associated with a single DMX control channel.  When the associated DMX channel passes through 50%, increasing, the lower (odd-numbered) relay shall close and be maintained while the higher (even-numbered) relay shall be open.  When the associated DMX channel passes through 50%, decreasing, the lower (odd-numbered) relay shall open, while the higher (even-numbered) relay shall close and be maintained.

2.1.6	Momentary Split with ‘Reset’ function.  Two sequential DMX channels are associated with each adjacent pair of relays.  When the lower DMX channel passes through 50%, increasing, the lower (odd-numbered) relay shall close for 100mSec.  When the lower DMX channel passes through 50%, decreasing, the higher (even-numbered) relay shall close for 100mSec.  The higher DMX channel shall provide secondary ‘reset’.  When the higher DMX channel passes through 50%, increasing, the higher (even-numbered) relay shall close for 100mSec.  When the higher DMX channel passes through 50%, decreasing, both relays shall remain unchanged.

2.1.7	Chase mode.  Each relay shall close for two seconds in a sequential pattern.  This function is intended for system testing.

2.2	The Module shall provide a relay output test mode to allow the user to activate a selected relay via the onboard user interface.

2.3	The Module shall include one additional Form-C relay output which shall function as a DMX-present detector.

2.4	The Module shall have a diagnostic mode, activated by pressing a pushbutton during power-up.

3.0	User Interface

3.1	A three-digit LED display and three pushbuttons shall provide the user interface to set DMX start address and operating mode, and to access test functions.

3.2	LED indicators shall provide status reporting for power, active processor, DMX input, and relay status.

3.3 	The module shall also be discoverable and configurable via a remote controller using RDM.

3.4	A DMX end-of-line termination switch shall be provided on the Module.

4.0 	Electrical

4.1	Multiple modules, up to the RS485 limitation of 32, may be daisy-chained on the same DMX input data line.

4.2	The power input shall be supplied by a Class 2 circuit. It shall accept a range of 9 to 30 volts DC and shall consume no more than 6 watts.

4.3	The DMX input port shall be capable of withstanding short-term application of up to 250V without damage to internal components.

4.4	Input protection shall be of the self-resetting type, rated for 250V.  Replaceable fuses shall not be acceptable.

4.5	The DMX input port shall provide 1500-volt optical isolation between the DMX signal and module electronics.

4.6	Each relay shall be rated for 100,000 operations at loads up to 2 amps / 30 VDC or 125 VAC. The module rating per relay shall be 1 amp @ 24V AC or DC.

4.7	Each relay output shall permit normally-open or normally-closed functionality.

4.8	All input, output and power connections shall utilize pluggable Phoenix-type screw terminal blocks, capable of accepting solid or stranded wire sizes from #26 to #16 AWG.

5.0	Protocol Compatibility

5.1	The input control signal shall be compatible with all variants of the lighting industry standard DMX512 control protocol.

5.2	One (1) DMX Pass-Thru port shall be provided. The Pass-Thru port shall be passive, that is, direct-wired from the input and not repeated, such that failure of the Module shall not adversely affect a signal being passed through to another module or device.

5.3	The Contact Closure module shall support RDM (Remote Device Management) for discovery and configuration.

5.4	It shall be possible to update the module’s firmware via the DMX port. Products that provide no firmware update capability will not be acceptable.

6.0	Physical

6.1	The Contact Closure module shall be designed to snap on to 35mm DIN rail without the use of tools.

6.2	The Module shall measure 3.6”W x 8.0”L x 1.5”H (91mm x  200mm x 38mm).

6.3	The Module shall weigh 0.7 lb. (316g).

7.0	Environmental

7.1	The ambient operating temperature shall be -10° to 50°C (14° to 122°F).

7.2	The storage temperature shall be -40° to 70°C (-40° to 158°F).

7.3	The operating humidity shall be 5% - 95% non-condensing.

8.0	Compliance

8.1	The Contact Closure Module shall meet the requirements of USITT DMX512 (1990), ANSI E1.11 DMX512-A, and ANSI E1.20 Remote Device Management.

8.2	The Contact Closure Module shall be compliant with the EU RoHS (2002/95/EC) directive.

8.3	The Contact Closure Module shall conform to all FCC and CE requirements.

8.4	The Contact Closure Module shall be powered by a UL1310 Class 2 low voltage circuit.

8.5	The module circuit board shall be manufactured from FR-4 glass epoxy laminate with a UL 94 flammability rating of V0. The board shall be clearly marked as such.

8.6	The module carrier housing shall be manufactured from extruded rigid PVC with a UL 94 flammability rating of 5VA.

7.0	Acceptable Product

7.1	The DMX Contact Closure Module(s) shall be Pathway Connectivity eDIN model #1003.